CAM – SER

DIGITAL TRANSMITTER FOR LOAD CELLS

Digital instrument to convert  the load cell signal to serial output  by Rs232 / Rs485/USB ports -  fully configurable.

Calibration procedure with theoretical method or with sample applied load.

Main parameters configuration in Stand Alone method by DIP/Switch selection

Full and detailed configuration by PC using custom software

## MAIN TECHNICAL FEATURES

| Voltage supply | 10 - 30 V dc |
| --- | --- |
| Power max | 1 W |
| Insulation | Class II |
| Installation category | Cat. II |
| Working Temperature | -10°C ( +50°C (humidity max 85% ) |
| Storage Temperature | -20°C ( +60°C |
| Dimensions | 55 mm x 90 mm x 58 mm (l x h x p) |
| Mounting | Omega Bar |
| Case material | Noryl UL 94V-0 self-extinguishing |
| Connections | Screwed Terminal Board and USB 2.0 Port |
| Linearity | <0.01% |
| Internal resolution | 24 bit |
| Load cell measurement range | from -3.9 mV/V to + 3.9mV/V |
| Acquisition frequency | 10 – 80 Hz |
| Digital filter | Selectable from 0.2 Hz to 50 Hz |
| Decimals | From 0 to 4 digital |
| Serial Ports | Rs232 half duplex; Rs422/Rs485 half duplex; USB Device |
|  | Serial protocol: ASCII, continuo stampabile, MODBUS |
| Baud rate | Until 115200 b/s - Default 9600 b/s - |
| Codes | EN61000-6-2, EN61000-6-3 for EMC |
|  | EN61010-1 Electrical Safety |